## Slide 1: Project 5: Sleep Position Classifier
Milan, 14 July 2022
Massimo Alfonzo
Chloé Canavate
Patrick Franke
Tutor: Giulia Alessandrelli
Professor: Pietro Cerveri

## Slide 2: Introduction
Objective
Classify 12 distinct sleep positions based on data gathered from two accelerometers
M. Alfonzo, C. Canavate, P. Franke
Using supervised and unsupervised machine learning techniques
Methodology

## Slide 3: Project outline
M. Alfonzo, C. Canavate, P. Franke
Hardware & Firmware
set up
Data visualization
and acquisition
Machine Learning
Breadboard V1
3-axis accelerations acquisition
PCB design
Casing design
Acquisition improved using FIFO
Data transmission via Bluetooth
3D printing & wires preparation
GUI development
for data acquisition
(12 positions)
Added live visualization of 6 acceleration channels
Data acquisition from 11 subjects
Visualization and pre-processing
Supervised classifier techniques
Unsupervised methods
Optimization of the parameters using CV
Prediction of the 4 master positions
Models comparison & best model selection

## Slide 4: Hardware
Components
M. Alfonzo, C. Canavate, P. Franke
Accelerometers
Bluetooth module
9 to 5 voltage regulator
PSoC microcontroller
9V battery

## Slide 5: Hardware – Breadboard
M. Alfonzo, C. Canavate, P. Franke

## Slide 6: Hardware – Breadboard
M. Alfonzo, C. Canavate, P. Franke
External wires connecting 2 accelerometers
Bluetooth module
Voltage regulator
9V to 5V
9V Battery

## Slide 7: PCB & Casing
M. Alfonzo, C. Canavate, P. Franke

## Slide 8: Hardware – Wearables
M. Alfonzo, C. Canavate, P. Franke
Ankle
Chest
2-meter long wires

## Slide 9: FIFO, I2C and Bluetooth communication
M. Alfonzo, C. Canavate, P. Franke
FIFO buffers
I2C communication
Bluetooth com.
Reduce CPU load
32 samples for each accelerometer
Set ODR = 10Hz
Switch to FIFO mode
Get 32 samples for each accelerometer
Send averaged data – string message
Baudrate 9600 bps

## Slide 10: Data acquisition protocol
M. Alfonzo, C. Canavate, P. Franke
Orientation
Place 1st accelerometer
on top of the chest
  Place 2nd accelerometer on the left ankle, on top of the external malleolus
At least 10 people
1 minute each position
Body placements
Data acquisition
20 seconds to switch position

## Slide 11: GUI for data acquisition and visualization
M. Alfonzo, C. Canavate, P. Franke

## Slide 12: Datasets
M. Alfonzo, C. Canavate, P. Franke
11 datasets
collected
features
target

## Slide 13
M. Alfonzo, C. Canavate, P. Franke
Machine Learning – Data visualization & cleaning
Raw data (before data cleaning)
Data after removing the first 20 transient samples

## Slide 14
M. Alfonzo, C. Canavate, P. Franke
Machine Learning – Data preparation pipeline
Outlier removal
Train & test splitting
Standardization
Subjects and/or positions with erroneous data
Led to 10 people
  4 females
  6 males
70/30 split stratified on the subject IDs
Training set: 7 people
Test set: 3 people
Scaler learned on train set and applied to both train and test sets
Dataset 1 - All the samples for the 6 coordinates
Dataset 2 - Averages, the min and the max of the 6 coordinates
Dataset 3 - Only the averages of the 6 coordinates
3 datasets
created

## Slide 15
M. Alfonzo, C. Canavate, P. Franke
Machine Learning – Overview of evaluated techniques

## Slide 16
M. Alfonzo, C. Canavate, P. Franke
Best for Supervised Learning: Random Forest
Machine Learning – Metrics and Results

## Slide 17
M. Alfonzo, C. Canavate, P. Franke
Machine Learning – Overview of evaluated techniques
ARI: Adjusted Rand Index
NMI: Normalized Mutual Information

## Slide 18
M. Alfonzo, C. Canavate, P. Franke
Best for Unsupervised Learning: K-means
Adjusted Rand Index: 0.27
Normalized Mutual
Information: 0.54
Machine Learning – Metrics and Results
WCSS: Within cluster sum of squares

## Slide 19
Accuracy: 100%
M. Alfonzo, C. Canavate, P. Franke
Machine Learning – Grouping to Master positions

## Slide 20
M. Alfonzo, C. Canavate, P. Franke
Future developments
Gather more data (subjects & sampling conditions)
Use additional sensors to distinguish between very similar positions
Implement real-time sleeping position classifier

## Slide 21: Project 5: Sleep Position Classifier
Milan, 14 July 2022
Massimo Alfonzo
Chloé Canavate
Patrick Franke
Tutor: Giulia Alessandrelli
Professor: Pietro Cerveri